## Slide 1: 2025 ENGINEERING INSTITUTION OF ZAMBIA SYMPOSIUM
OPTIMISING COLLECTOR AZIMUTH AND TILT FOR EVENING HOT WATER DEMAND IN HYBRID SOLAR GEYSERS
PRESENTER : Amos Banda
DATE : Friday 17th April 2026
Avani Victoria Falls Resort, Livingstone, Zambia

## Slide 2
The Problem Statement
  The "North" Orthodoxy: Standard practice dictates a 0° Azimuth (True North) to maximize annual yield.
  The Mismatch: Maximum production occurs at solar noon, while peak demand occurs in the morning and evening.
  The Consequence: Reliance on 4,000W electric auxiliary heaters during peak grid hours (25% - 40% of household consumption).
Typical Distribution Curves of Solar Radiation and Wind Speed through out a Day (Source: X. Liu & Z. Bie)

## Slide 3
Research Objective
Primary Goal: Identify the optimal North-West collector orientation that maximizes thermal energy retention.
Target: Minimize reliance on auxiliary electric heating during late-afternoon and evening periods.

## Slide 4
Methodology – The Model
Single-Node Thermal Model: Used to simplify transient energy balance while maintaining accuracy.
Energy Balance Equation:
Schematic Diagram of a Hybrid Solar Water Heater
Data Source: Meteosat Prime Meridian Africa (4km resolution) for Global Horizontal Irradiance (GHI) and Direct Normal Irradiance (DNI).

## Slide 5
Hot Water Draw Profile
Consumption Event: One large draw representing four adult showers.
Total Draw Volume (Vdraw): 200 Liters (four showers at 50 Liters each of hot water).
Time of Draw Variation: To assess the impact of demand-side management and load-shifting strategies, the simulation will be executed across three distinct time slots for the 200 Litre draw i.e morning, afternoon and evening.

## Slide 6
System Specifications
Collector Type: Evacuated Tube (High-efficiency).
Collector Area: 3.0 m2 (Sized for a 200L system).
Auxiliary Power: 4,000 W (Standard element rating).

## Slide 7
Selecting the "Worst-Case" Scenario
The "Stress Test": Ambient temperature low of 7.6 °C.
Typical Meteorological Year (TMY): Analysis focused on the coldest winter day (Winter Solstice, June 21st).

## Slide 8
Solar Radiation Profiles

## Slide 9
Solar Radiation Profiles
Baseline (0° Azimuth):
Maximum irradiance occurs early, around 10:00 hrs.

## Slide 10
Solar Radiation Profiles
The Shift:
As the azimuth increases towards the West, afternoon radiation improves significantly.

## Slide 11
Solar Radiation Profiles
Chart: True West irradiance @ Varying Tilt Angles
| 44733 | 44733.041666666664 | 44733.083333333336 | 44733.125 | 44733.166666666664 | 44733.208333333336 | 44733.25 | 44733.291666666664 | 44733.333333333336 | 44733.375 | 44733.416666666664 | 44733.458333333336 | 44733.5 | 44733.541666666664 | 44733.583333333336 | 44733.625 | 44733.666666666664 | 44733.708333333336 | 44733.75 | 44733.791666666664 | 44733.833333333336 | 44733.875 | 44733.916666666664 | 44733.958333333336

5° | 0 | 0 | 0 | 0 | 0 | 36.8659 | 241.8478 | 242.5409 | 347.3537 | 477.7164 | 961.3476 | 546.649 | 477.1356 | 822.9722 | 622.2183 | 320.0226 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
15° | 0 | 0 | 0 | 0 | 0 | 0 | 122.453 | 235.7578 | 337.9061 | 462.4651 | 896.4418 | 537.6759 | 473.6055 | 865.909 | 685.0613 | 374.0442 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
25° | 0 | 0 | 0 | 0 | 0 | 0 | 0.45656 | 225.8354 | 323.7563 | 440.0151 | 805.9484 | 520.005 | 462.6685 | 887.2943 | 730.7267 | 418.3032 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
35° | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 213.0502 | 305.2678 | 410.8744 | 691.5319 | 494.1732 | 444.7727 | 887.9285 | 758.9942 | 451.9084 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
45° | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 197.767 | 282.9383 | 375.7576 | 555.5897 | 460.9653 | 420.577 | 869.2148 | 770.127 | 474.2654 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
55° | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 180.4286 | 257.3858 | 335.5655 | 401.1807 | 421.3902 | 390.9309 | 833.1055 | 764.8467 | 485.0859 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
65° | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 161.5427 | 229.3307 | 291.3591 | 231.9348 | 376.6504 | 356.8484 | 782.0326 | 744.2957 | 484.3866 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
75° | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 141.667 | 199.5748 | 244.3286 | 51.9452 | 328.1051 | 319.4773 | 718.8233 | 709.9867 | 472.4816 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
85° | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 121.3925 | 168.9776 | 195.758 | 0 | 277.2292 | 280.0633 | 646.6046 | 663.7443 | 449.9656 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Tilt Optimisation:
The 5° tilt angle had the best morning radiation, while the 55° had the best afternoon radiation.

## Slide 12
Solar Radiation Profiles
An inclined surface facing west receives more radiation in the afternoon hours compared to the one facing north.
A west-facing solar receptor surface is better optimised for receiving afternoon radiation.

## Slide 13
Tank Temperature Profiles
No Draw Heating Scenarios
The geyser facing north was able to achieve a temperature of 49°C against 47°C for the west-facing geyser.
If the same no-draw scenario above is applied but this time with auxiliary heating in the early hours, the two geysers perform basically the same and will keep the temperature around 63°C by midnight.

## Slide 14
Tank Temperature Profiles
The "Three Draw" Scenario
Testing Real Use: Morning, Afternoon, and Evening draws of 200L total.
Morning Draw Performance: North is slightly more efficient (10.9 kWh vs. 11.9 kWh for West).
Afternoon Draw Performance: West consumes 6.8 kWh vs. North's 7.7 kWh.
The Result: A 10% reduction in electrical energy consumption for afternoon/evening demand.

## Slide 15
Conclusion & Recommendations
Conclusion:
A geyser facing the true west (90°) and tilted at an angle of 55° will receive more radiation in the afternoon than a geyser facing true north (0°) and tilted at 15°.
The rate of solar heating during the afternoon hours is higher for a west-facing geyser.
The west-facing geyser required 10% less electrical energy to reheat the water compared to the north-facing geyser.
Orienting a solar geyser at a 90° azimuth angle and a 55° tilt angle optimizes the performance of a hybrid geyser for afternoon hot water consumption.

## Slide 16
Conclusion & Recommendations
Future Work:
A high-fidelity thermal analysis employing the multi-node model be conducted.
An integrated dynamic flow control should be investigated with the aim of retaining the hot temperature for the top layer during draws.

## Slide 17
Thank You