## Slide 1
Engineering Institution of Zambia
Annual Symposium 2026
P05
Analysis of Forest Cover Dynamics in Lusaka East Forest Using Multi‑Sensor Remote Sensing and GIS Integration
Lusaka East Forest Reserve No. 27 | 2013 – 2024
Nachaambwa Miyanda Moonga | +260 76 989 0265
Co-Author: Michael Mutale | +260 96 254 9674
Submitted to: EIZ Symposium 2026

## Slide 2
Presentation Outline
2 / 14
1
Background & Significance
2
Study Area
3
Research Objectives
4
Data & Methodology
5
NDVI Classification Results
6
Land Cover Change Analysis
7
Key Findings & Discussion
8
Conclusions & Future Work
Study focus: Lusaka East Forest Reserve No. 27 | 2013 – 2024 | Landsat Collection 2 · 30 m resolution

## Slide 3
Background & Significance
3 / 14
Urban forests under pressure. Rapid urbanisation in sub-Saharan Africa is driving forest encroachment and informal settlement expansion on peri-urban reserves.
Lusaka's growth trajectory. Zambia's capital is one of Africa's fastest-growing cities, with population growth directly threatening adjacent forest reserves.
NDVI as a monitoring tool. Vegetation indices derived from satellite imagery provide a systematic, repeatable method for land cover change detection at landscape scale.
11-year Landsat time series. Landsat Collection 2 imagery (2013–2024) at 30 m resolution enables evidence-based assessment of forest degradation trends over time.
Global tropical deforestation: ~10 million ha/year — local-scale monitoring is critical (FAO, 2022)

## Slide 4
Study Area — Lusaka East Forest Reserve No. 27
4 / 14
Study Area Boundary
Landsat imagery — 30 m spatial resolution
Site Profile
~1,788 ha
Total mapped area
1,756 ha
Classified pixels
~15 km
East of Lusaka CBD
Chalimbana
Sub-catchment
Miombo
Woodland ecosystem
30 m / 5 yrs
Resolution / time-steps

## Slide 5
Research Objectives & Methodology
5 / 14
Objectives
1
Map land cover across Lusaka East Forest Reserve No. 27 for 2013–2024
2
Classify five NDVI-based vegetation classes from Landsat Collection 2 Level-2 imagery
3
Quantify built-up expansion and dense vegetation loss using pixel-based statistics
4
Identify spatial patterns of encroachment and forest degradation
Methodology
Data Acquisition
Landsat C2 T1 Level-2 — dry season composites (Jun–Aug), 5 epochs
2. Preprocessing
DN × 0.0000275 − 0.2 → Surface Reflectance (Collection 2 scale factor)
3. Index Computation
NDVI, MNDWI, NDBI, BSI calculated per epoch
4. Hybrid Classification
Majority-vote built-up mask (≥ 2 of 3: NDBI > 0.05, BSI > 0, NDVI < 0.20)
5. Change Analysis
Cross-tabulation pixel statistics — 2013 baseline vs. 2024 final

## Slide 6
Hybrid NDVI Classification Approach
6 / 14
Classification Priority
1
Water MNDWI > 0
2
Built-up Dry-season: NDBI > 0.05, BSI > 0, NDVI < 0.20
(majority-vote ≥ 2 of 3 conditions)
3
Dense Veg. NDVI ≥ 0.40 (annual median composite)
4
Moderate Veg. NDVI 0.25 – 0.40
5
Sparse Veg. NDVI 0.10 – 0.25
6
Bare / Residual NDVI < 0.10
Miombo context: Wet-season grass inflates NDVI on built-up plots — dry-season sub-composite prevents misclassification (Frost, 1996)
Spectral Indices
NDVI
(NIR − Red)
──────────────
(NIR + Red)
MNDWI
(Green − SWIR1)
──────────────
(Green + SWIR1)
NDBI
(SWIR1 − NIR)
──────────────
(SWIR1 + NIR)
BSI
((SWIR1+Red) − (NIR+Blue))
─────────────────────
((SWIR1+Red) + (NIR+Blue))

## Slide 7
NDVI Land Cover Classification — 2013 · 2016 · 2019
7 / 14
2013
2016
2019
Landsat Collection 2 Tier 1 Level-2 · 30 m resolution · Annual median composite · 5-class NDVI scheme

## Slide 8
NDVI Land Cover Classification — 2022 & 2024
8 / 14
2022
2024
Key observation: By 2024, built-up and bare surfaces have expanded markedly along the northern and southern reserve boundaries. The 2024 map (right) also encodes the 2013–2024 change layer, revealing encroachment hotspots in pink/magenta.

## Slide 9
Land Cover Change Analysis — 2013 vs. 2024
9 / 14
Change: 2013 → 2024
Pink = Built-up expansion · Green = Revegetation · White = No change
Pixel-Level Statistics (n = 20,789 pixels each)
Built-up Expansion (vs. 2013)
9.5%
1,976 px
Expansion
4.1%
847 px
Re-vegetated
86.4%
17,966 px
No Change
Dense Vegetation Change (vs. 2013)
7.2%
1,488 px
Veg. Loss
2.2%
450 px
Veg. Gain
90.7%
18,851 px
No Change
Dense vegetation loss : gain ratio > 3 : 1 — indicating net canopy decline

## Slide 10
NDVI Land Cover Class Area Trends — 2013 to 2024
10 / 14
Panel A — Moderate Vegetation (dominant class, ~1,000–1,300 ha) · Panel B — Dense, Sparse, Bare/Built-up, Water (0–400 ha)

## Slide 11
Key Findings & Discussion
11 / 14
-47.1%
Dense Vegetation
185 ha → 98 ha (2013–2024)
+53.2%
Built-up Expansion
+90.34 ha net change
85.0%
Total Veg. Cover Remaining
(was 90.1% in 2013)
Urban Expansion Pattern
Encroachment concentrated along northern and southern reserve boundaries; built-up expansion (9.5%) far outpaced revegetation (4.1%).
Forest Transition Theory
A loss:gain ratio >3:1 for dense vegetation is consistent with early urbanisation phases described by Rudel et al. (2020) — extraction precedes any recovery.
Miombo Woodland Challenge
Seasonal grass in miombo woodland inflates NDVI on built-up plots — the hybrid dry-season classification approach directly addresses this ecological challenge (Frost, 1996).
Policy Relevance
Spatial evidence supports targeted conservation in alignment with Zambia's Forestry Act and National Climate NDC commitments (Ministry of Lands, 2025).

## Slide 12
Conclusions & Future Work
12 / 14
Conclusions
1
Dense vegetation declined 47.1% (185 → 98 ha) while built-up area expanded 53.2% (+90 ha) over 2013–2024.
2
Total vegetation cover fell from 90.1% to 85.0%, indicating measurable forest degradation.
3
Encroachment concentrated along the northern and southern reserve boundaries.
4
Landsat hybrid NDVI classification effectively distinguished built-up from miombo woodland.
5
Remote sensing confirms the reserve is under significant and ongoing urban pressure.
Future Work
Participatory Mapping
Engage communities to verify encroachment boundaries and drivers on the ground
Policy Evaluation
Assess enforcement effectiveness under Zambia's Forestry Act
Restoration Modelling
Identify priority zones for active revegetation interventions
Climate Integration
Separate climate from anthropogenic drivers using rainfall and temperature data

## Slide 13
Key References
13 / 14
1
FAO (2025). Global Forest Resources Assessment 2025. Food and Agriculture Organization of the United Nations, Rome.
2
Frost, P.G.H. (1996). The ecology of miombo woodlands. In B. Campbell (Ed.), The Miombo in Transition (pp. 11–55). CIFOR.
3
Hansen, M.C. et al. (2013). High-resolution global maps of 21st-century forest cover change. Science, 342(6160), 850–853.
4
Phiri, D. & Morgenroth, J. (2017). Developments in Landsat land use/land cover analysis. Remote Sensing, 9(9), 967.
5
Pettorelli, N. et al. (2005). Using the satellite-derived NDVI to assess ecological responses to environmental change. Trends in Ecology & Evolution, 20(9), 503–510.
6
Rudel, T.K. et al. (2020). The global pattern of forest transitions. Global Environmental Change, 63, 102080.
7
Tembo, E. & Volk, M. (2022). Land use and land cover change in a peri-urban area in Zambia. Land, 11(4), 574.
8
Wulder, M.A. et al. (2012). Opening the archive: How free data enabled the Landsat monitoring promise. Remote Sensing of Environment, 122, 2–10.
9
Ministry of Lands and Natural Resources (2025). Zambia Forestry Act and National Forest Policy. Government of Zambia.

## Slide 14
Thank You
Questions & Discussion
Nachaambwa Miyanda Moonga | +260 76 989 0265
Co-Author: Michael Mutale | +260 96 254 9674
Engineering Institution of Zambia · Annual Symposium 2026
EIZ — Engineering Institution of Zambia